## Slide 1: Water Quality Monitoring on Larkin Creek St. Francis County, AR
JL Bouldin
RA Warby
Arkansas State University

## Slide 2: Background
Larkin Creek is a tributary of the L’Anguille River
  dominated by row crop agriculture.
L’Anguille River is a tributary of the St. Francis River in eastern Arkansas in the Delta ecoregion
ADEQ authorized the St. Francis County Conservation District to implement BMPs to reduce pollutant loading to L’Anguille

## Slide 3: Site description
Lateral 1-A of Larkin Creek
  Tributary of the L’Anguille River
  HUC#080202050506
St. Francis County

## Slide 4: Site description
St. Francis County

## Slide 5: Site description
Lateral 1-A of Larkin Creek
  Tributary of the L’Anguille River
  HUC#080202050506

## Slide 6: BMPs
St. Francis County Conservation District
sediment pond construction
plant riparian buffers
remove sediment
restore the channel
  Lateral 1-A of Larkin Creek
L’Anguille River
Agricultural activities cited as major cause of the impairment within watershed
  excessive turbidity from silt, suspended solids loading, sedimentation

## Slide 7: Objectives
Determine baseline data prior to BMP implementation
Weekly grab samples
Total Suspended Solids
pH
Dissolved Oxygen
Nutrients
  Nitrate, Nitrite, Orthophosphate

## Slide 10: Upper Larkin Creek site
Upstream
Downstream

## Slide 11: Middle Larkin Creek site
Upstream
Downstream

## Slide 12: Lower Larkin Creek site
Upstream
Downstream

## Slide 13: TSS at all sites

## Slide 14: Preliminary results
TSS highest at Middle Site
  Especially following rain events
  Will benefit from upstream sedimentation pond
pH lowest at Upper and Middle sites from temporary acidification following rain events
DO high due to increased primary production and early afternoon sampling times
Final sampling and nutrient data pending

## Slide 15
Questions?
Upper Larkin Creek
Lower Larkin Creek
Middle Larkin Creek